Milestone 5:

Without thermostate:

without using thermostate the temperature goes up (from 0 to 0.904225 then it goes down again! ) and potential energy goes down (from -41.1777 to -77.7983 then it goes up again!)

decreasing the lattice constant (from 1 to 0.5) I can see the evaporation is getting faster than if it”s 1
and temp increases (0 to 117744 and stay still) and the same for potentisl energy (from 5.85172e+06 to -0.00191873

With thermostate:

Relaxation number
 Pick one that is slow enough to allow the system to relax but fast enough to avoid evaporation.

small relaxation >> strong temperature coupling and faster going to desired temperature but very slow to get to the equilibrium point ( small potential energy)

big relaxation >> little coupling, very slow to reach desired temp but very fast to equilibrium ( but it will evaporate)

lattice constant (with or eithout thermostate):
if small (smaller than 1) then more potential energy and more speed and if bigger less velocity

two ways to adapt relaxation factor:
1- based on temp: if desired temp – current temp < 0.01 increase relaxation factor by 0.1 and if not decrease if by 0.1

if (abs(desired_temperature - energy.get_temperature()) <= 0.01 && energy.get_temperature() != 0.0) {
   relaxation_time_multiplier += 0.1;
}
else {
   relaxation_time_multiplier <= 1.0 ? relaxation_time_multiplier = 1.0 : relaxation_time_multiplier -= 0.1;
}

2- based on potenetial energy:
if old potential – current potential < 1 then increase the relaxation factor to 10

if (abs(energy.get_potential_energy() - old_potential_energy) <= 1.0) { // reached equilibrium point, decrease coupling constant
   relaxation_time_multiplier = 10;
}