Milestone 5:

Without thermostate:

without using thermostate the temperature goes up (from 0 to 0.904225 then it goes down again! ) and potential energy goes down (from -41.1777 to -77.7983 then it goes up again!)

decreasing the lattice constant (from 1 to 0.5) I can see the evaporation is getting faster than if it”s 1
and temp increases (0 to 117744 and stay still) and the same for potentisl energy (from 5.85172e+06 to -0.00191873

With thermostate:

Relaxation number
 Pick one that is slow enough to allow the system to relax but fast enough to avoid evaporation.

small relaxation >> strong temperature coupling and faster going to desired temperature but very slow to get to the equilibrium point ( small potential energy)

big relaxation >> little coupling, very slow to reach desired temp but very fast to equilibrium ( but it will evaporate)

lattice constant (with or eithout thermostate):
if small (smaller than 1) then more potential energy and more speed (more likely to evaporate faster)
>> smallest constant possible is 0.8 (less than that it will evaporate very very fast)

two ways to adapt relaxation factor:
1- based on temp: if desired temp – current temp < 0.01 increase relaxation factor by 0.1 and if not decrease if by 0.1

if (abs(desired_temperature - energy.get_temperature()) <= 0.01 && energy.get_temperature() != 0.0) {
   relaxation_time_multiplier += 0.1;
}
else {
   relaxation_time_multiplier <= 1.0 ? relaxation_time_multiplier = 1.0 : relaxation_time_multiplier -= 0.1;
}

2- based on total energy:
if old total – current total < 1 then increase the relaxation factor to 50

if (abs(energy.get_total_energy() - old_total_energy) <=
   1.0) { // reached equilibrium point, decrease coupling constant
   relaxation_time_multiplier = 50;
}

time analysis:
total time = 5000
time_step = 1/1000
lattice_constant = 0.8
relaxation_time = 10 * time_step then increases to 50 after equilibrium (based on total energy)
real and user times meanings

Number of atoms	9	27	64	100	125	150	216	294
Time (s)	real 0m1.077s / user 0m0.874s / sys 0m0.057s	real 0m7.705s / user 0m7.127s / sys 0m0.189s	real 0m35.877s / user 0m35.168s / sys 0m0.393s	real 1m27.949s / user 1m25.186s / sys 0m0.596s	real 2m19.785s / user 2m15.673s / sys 0m0.771s	real 3m0.663s / user 2m57.534s / sys 0m0.703s	real 5m57.855s / user 5m50.970s / sys 0m1.152s	real 10m51.011s / user 10m43.855s / sys 0m1.116s
Real time in (s)	1.077	7.705	35.87	87.949	139.785	180.663	357.855	651.011

atom numbers vs time
atom numbers
time (s)

test strategy:
it’s just checking if the temperature really converge after some time to the desired value or not (test for lattice of 1 atom and lattice of 5x5x5)

Milestone 6:

time analysis:
same as mielstone 5:
total time = 5000
time_step = 1/1000
lattice_constant = 0.8
relaxation_time = 10 * time_step then increases to 50 after equilibrium (based on total energy)
cutoff_radius = 1.5

Number of atoms	9	27	64	100	125	150	216	294
Time (s)	real 0m6.616s / user 0m3.450s / sys 0m0.303s	real 0m11.188s / user 0m10.654s / sys 0m0.228s	real 0m34.987s / user 0m33.689s / sys 0m0.352s	real 0m53.658s / user 0m52.865s / sys 0m0.416s	real 1m11.675s / user 1m9.782s / sys 0m0.651s	real 1m17.554s / user 1m16.861s / sys 0m0.552s	real 2m6.615s / user 2m5.150s / sys 0m0.773s	real 2m57.393s / user 2m55.774s / sys 0m1.069s
Real time in (s)	6.616	11.188	34.987	53.658	71.675	77.554	126.615	177.393

Atom number vs time
atom number
time

Notes: it’ linear instead of squared curve, the time until almost 60 atoms is better in the first diagram >> that means that the neighboring algorithm is bad for small number of atoms
Note: tried with cuttoff = 2 and it was bad in all times!!